LU150/ED23.5

ANSI Designation ：S55

Performance Data Light Output (Lumens@100Hrs.) 14000lm Lamp Lumens Per Watt 95lm/W Rated Life(Hrs.@ 10 Hr.I Start) 12000hrs Correlated Color Temperature K 2000K Color Rendering Index(CRI) Typical Warm Up Time(Minutes) 3-5 Typical Hot Restart Time(Minutes) 8-12 Burning Position UNIVERSAL

Physical Data/Requirements Base Designation E39 Bulb Designation ED23.5 Bulb Diameter 76mm Max. Overall Length (MOL) 197mm Light Center Length(LCL) 127±3mm Max Base Temperature 210℃ Max.Bulb Temperature 400℃ Luminaire Type MNCLOSED Socket Style MED Electrical Data/Requirements Lamp Wattage 150W Operating Voltage 45~64V Operating Current(Amps) 3.2A Packing size: Description of goods Quantity/ctn Measurement (cm) G.W. N.W. LU150/ED23.5 12 13.5*10*9 in 3.8 3.0 ce 1.80A 95DIUM