LU250/ET18

ANSI Designation ：S50

Performance Data Light Output (Lumens@100Hrs.) 25000lm Lamp Lumens Per Watt 100lm/W Rated Life(Hrs.@ 10 Hr.I Start) 12000hrs Correlated Color Temperature K 2000K Color Rendering Index(CRI) Typical Warm Up Time(Minutes) 3-5 Typical Hot Restart Time(Minutes) 8-12 Burning Position UNIVERSAL

Physical Data/Requirements Base Designation E39 Bulb Designation ET18 Bulb Diameter 57mm Max. Overall Length (MOL) 248mm Light Center Length(LCL) 146±3mm Max Base Temperature 210℃ Max.Bulb Temperature 400℃ Luminaire Type MNCLOSED Socket Style MOGUL Electrical Data/Requirements Lamp Wattage 250W Operating Voltage 77~120V Operating Current(Amps) 3.0A Packing size: Description of goods Quantity/ctn Measurement (cm) G.W. N.W. LU250/ET18 12 11*8.5*11 in 4.2 3.5 ce 1.80A 95DIUM