MH70/ED17/U/PS/4K/MED (3)

ANSI Designation ：M98

Performance Data Light Output(Lumens@100Hrs.) 5600lm Lamp Lumens Per Watt 80lm/W Rated Life(Hrs.@ 10 Hr.I Start) 6000hrs Correlated Color Temperature K 4000K Color Rendering Index(CRI) 65 Typical Warm Up Time(Minutes) 3-5 Typical Hot Restart Time(Minutes) 8-12 Burning Position UNIVERSAL

Physical Data/Requirements Base Designation E26 Bulb Designation ED17 Bulb Diameter 54mm Max. Overall Length (MOL) 141mm Light Center Length(LCL) 86±3mm Max Base Temperature 190℃ Max.Bulb Temperature 400℃ Luminaire Type MNCLOSED Socket Style MEDIUM Electrical Data/Requirements Lamp Wattage 70W Operating Voltage 75~100V Operating Current(Amps) 0.9A Packing size: Description of goods Quantity/ctn Measurement (cm) G.W. N.W. MH70/ED17/U/PS/4K/MED 48 14.4*9.8*14.0 in 1.9 1.5 ce 1.80A 95DIUM