MH320/BT37/BU/PS/4K (23)

ANSI Designation ：M154

Performance Data Light Output(Lumens@100Hrs.) 28800lm Lamp Lumens Per Watt 90lm/W Rated Life(Hrs.@ 10 Hr.I Start) 12000hrs Correlated Color Temperature K 4000K Color Rendering Index(CRI) 65 Typical Warm Up Time(Minutes) 3-5 Typical Hot Restart Time(Minutes) 8-12 Burning Position UNIVERSAL

Physical Data/Requirements Base Designation E39 Bulb Designation BT37 Bulb Diameter 89mm Max. Overall Length (MOL) 292mm Light Center Length(LCL) 181±6mm Max Base Temperature 210℃ Max.Bulb Temperature 400℃ Luminaire Type MNCLOSED Socket Style MOGUL Electrical Data/Requirements Lamp Wattage 320W Operating Voltage 118~148V Operating Current(Amps) 2.63A Packing size: Description of goods Quantity/ctn Measurement (cm) G.W. N.W. MH320/BT37/BU/PS/4K 12 20.1*15.0*12.6 in 1.9 1.5 ce 1.80A 95DIUM