MH400/ED37/C/U/4K (30)

ANSI Designation ：M59

Performance Data Light Output(Lumens@100Hrs.) 34000lm Lamp Lumens Per Watt 85lm/W Rated Life(Hrs.@ 10 Hr.I Start) 12000hrs Correlated Color Temperature K 3800K Color Rendering Index(CRI) 65 Typical Warm Up Time(Minutes) 3-5 Typical Hot Restart Time(Minutes) 8-12 Burning Position UNIVERSAL

Physical Data/Requirements Base Designation E39 Bulb Designation ED37 Bulb Diameter 118mm Max. Overall Length (MOL) 292mm Light Center Length(LCL) 181±6mm Max Base Temperature 210℃ Max.Bulb Temperature 400℃ Luminaire Type MNCLOSED Socket Style MOGUL Electrical Data/Requirements Lamp Wattage 400W Operating Voltage 118~148V Operating Current(Amps) 3.25A Packing size: Description of goods Quantity/ctn Measurement (cm) G.W. N.W. MH400/ED37/C/U/4K 12 20.1*15.0*12.6 in 1.9 1.5 ce 1.80A 95DIUM